## Slide 1: Computer-System Structures

## Slide 2: A Modern Computer System

## Slide 3: Computer-System Operation
I/O devices and the CPU can execute concurrently
Each device controller is in-charge of a particular device type
Each device controller has a local buffer
CPU moves data from/to main memory to/from local buffers
I/O is from the device to local buffer of controller
Device controller informs CPU that it has finished its operation by causing an interrupt

## Slide 4: Common Functions of Interrupts
Interrupt transfers control to the interrupt service routine , through the interrupt vector, which contains the addresses of all the interrupt service routines
Interrupt architecture must save the address of the interrupted instruction
An operating system is interrupt driven

## Slide 5: Interrupt Handling
The operating system preserves the state of the CPU by storing registers and the program counter
Determines which type of interrupt has occurred:
  Vectored
  Non vectored
Separate kernel routines determine what action should be taken for each type of interrupt

## Slide 6: I/O Structure
Synchronous I/O - After I/O starts, control returns to user program only upon I/O completion
Asynchronous I/O - After I/O starts, control returns to user program without waiting for I/O completion
Device-status table contains entry for each I/O device indicating its type, address, and state
Operating system access I/O device table to determine device status and to modify table entry

## Slide 7: Two I/O Methods
Synchronous
Asynchronous

## Slide 8: Device-Status Table

## Slide 9: Direct Memory Access Structure
Device controller transfers blocks of data from buffer storage directly to main memory without CPU intervention
Only one interrupt is generated per block, rather than the one interrupt per byte

## Slide 10: Storage Structure
Main memory – only storage media that the CPU can access directly
Secondary storage – extension of main memory that provides large nonvolatile storage capacity
Magnetic disks – rigid metal or glass platters covered with magnetic recording material
  Disk surface is logically divided into tracks, which are subdivided into sectors
  The disk controller determines the logical interaction between the device and the computer

## Slide 11: Storage Hierarchy
Storage systems organized in hierarchy
  Speed
  Cost
  Volatility
  Size
Caching – copying information into faster storage system; main memory can be viewed as a last cache for secondary storage

## Slide 12: Storage-Device Hierarchy

## Slide 13: Caching
Use of high-speed memory to hold recently-accessed data
Requires a cache management policy
Caching introduces another level of complexity in storage hierarchy.
  This requires data that is simultaneously stored in more than one level to be consistent

## Slide 14: Hardware Protection
Dual-Mode Operation
I/O Protection
Memory Protection
CPU Protection

## Slide 15: Dual-Mode Operation
Sharing system resources , requires operating system to ensure that an incorrect program or miss behaving user, cannot cause other programs to execute incorrectly
OS must provide hardware support to differentiate between at least two modes of operations
  1. User mode – execution done on behalf of a user
  2. Monitor mode (also kernel mode or system mode) – execution done on behalf of operating system

## Slide 16: Dual-Mode Operation (Cont.)
Mode bit added to computer hardware to indicate the current mode: monitor (0) or user (1)
When an interrupt or fault occurs hardware switches to monitor mode
Privileged instructions can be issued only in monitor mode
monitor
user
Interrupt/fault
set user mode

## Slide 17: I/O Protection
All I/O instructions are privileged instructions
Must ensure that a user program could never gain control of the computer in monitor mode (i.e., a user program that, as part of its execution, stores a new address in the interrupt vector)

## Slide 18: Read data from hard disk
Read data from
cyl= 5 , sec =10 head = 2
Application 1
Cyl= 5;
Sec=10;
Head=2
Get data
Read data from
cyl= 20 , sec =5 head = 1
Application 2
Cyl=20;
Sec=5;
head;=1
Get data

## Slide 19: Memory Protection
Must provide memory protection at least for the interrupt vector and the interrupt service routines
In order to have memory protection, at a minimum add two registers that determine the range of legal addresses a program may access:
  Base register – holds the smallest legal physical memory address
  Limit register – contains the size of the range
Memory outside the defined range is protected

## Slide 20: Use of A Base and Limit Register

## Slide 21: Hardware Address Protection

## Slide 22: Hardware Protection
When executing in monitor mode, the operating system has unrestricted access to both monitor and user’s memory
The load instructions for the base and limit registers are privileged instructions

## Slide 23: Timer
Timer – interrupts computer after specified period to ensure operating system maintains control
  Timer is decremented every clock tick
  When timer reaches the value 0, an interrupt occurs
Timer commonly used to implement time sharing
Time also used to compute the current time
Load-timer is a privileged instruction

## Slide 24: General-System Architecture
Given the I/O instructions are privileged, how does the user program perform I/O?
System call – the method used by a process to request action by the operating system
  Usually takes the form of a trap to a specific location in the interrupt vector
  Control passes through the interrupt vector to a service routine in the OS, and the mode bit is set to monitor mode
  The monitor verifies that the parameters are correct and legal, executes the request, and returns control to the instruction following the system call